## Slide 1: INJECTION MOLDING MACHINE
Professional Technical Guide
Industrial Manufacturing
How to Select the Right Injection Molding Machine
January 2026
From Requirements to Machine Selection
Qingdao HEE&HATO Technology Co., Ltd.
HEE&HATO

## Slide 2: Why Injection Machine Selection Matters
INTRODUCTION
Core Issue
Injection molding machine selection directly affects production efficiency, product quality, and cost control.Scientific selection is the prerequisite for efficient manufacturing.
Experienced Customers
Customers with extensive experience can independently evaluate and select machines based on their own production requirements, with deep understanding of equipment and processes.
Manufacturer Support
When only samples or preliminary concepts are available, or when special product requirements exist, professional manufacturers are required to provide technical support and machine selection recommendations.
Special Product Requirements
Special products may require dedicated configurations such as accumulators, closed-loop control, or injection compression.
These configurations require professional evaluation and customization.
Accumulator
Closed Loop
Injection Compression
Scientific machine selection is the foundation of efficient production.
Proper equipment matching maximizes manufacturing efficiency.

## Slide 3: Key Information to Collect Before Machine Selection
KEY INFORMATION
Four Core Dimensions · Complete Data Collection
Mold Information
Dimensions
Width × Height × Thickness (mm)
Weight
Total mold weight (kg)
Special Design
Slides, lifters, hot runner, etc.
Plastic Material Information
Type
PP, ABS, PC, PA, etc.
Quantity
Single material or multi-material
Properties
Flowability, shrinkage, corrosion
Product Information
Overall Dimensions
Length × Width × Height × Wall Thickness (mm)
Weight
Single part weight (g)
Cavity Number
Cavities per mold & layout
Molding Requirements
Quality Standards
Precision grade, surface finish, tolerance
Production Rate
Cycle time requirements, output target
Special Requirements
High speed, high precision, multi-color, etc.
Important Note：Complete and accurate information collection is the foundation of scientific machine selection.
Missing any dimension may lead to incorrect selection.

## Slide 4: SELECTION STEP 1: Basic Matching
SELECTION STEP 1
Step 1 · Choose the Right Type | Step 2 · Ensure Mold Fit
01
Choose the Right Machine Type
Determine Machine Type / Series
Based on product type + plastic material
Thermoplastics
Thermoset (Bakelite)
PET
Other special materials
Molding Type
Single-color
Two-color
Multi-color
Match special requirements with dedicated series
High stability – Closed loop
Ultra-high speed
Ultra-high speed
Multi-circuit
02
Ensure Mold Fit
Define Basic Clamping Unit Parameters
1 Mold width/height ≤ tie-bar spacing
At least one dimension must satisfy
2 Mold width/height within platen size range
Must not exceed platen boundary
3 Mold thickness within mold thickness range
Min mold thickness ≤ Actual ≤ Max mold thickness
4 Meets minimum mold size requirement
Avoid mold being too small
Matching Principles
Machine–product matching
Dimension verification
Ensure mold can be properly installed
Four-point confirmation
Comprehensive compatibility verification

## Slide 5: SELECTION STEP 2: Ejection & Clamping
SELECTION STEP 2
Step 3 · Ejection Capability | Step 4 · Clamping Force
03
Ejection Capability
Define Mold Opening Stroke / Ejector Stroke
Mold Opening Stroke
≥ (Product height × 2) + sprue length
Ensure the product can be removed smoothly
Ejector Stroke
Must be sufficient to eject the product
Ensure the part can fully release from the cavity
04
Clamping Force
Determine Required Clamping Tonnage
1 Calculate Projected Area
Projected area of the product in the mold opening direction (cm²)
Including cavity number and runner system
2 Calculate Mold Separation Force
Projected area × cavity number × cavity pressure
Typical materials: 350–400 kg/cm²
3 Determine Clamping Force
Mold separation force × 1.17
Safety factor 17%
Key Principle：Clamping force must be sufficient to prevent mold flash,
while avoiding excessive oversizing that leads to cost waste.

## Slide 6: SELECTION STEP 3: Injection Unit Matching
SELECTION STEP 3
Step 5 · Shot Capacity | Step 6 · Injection Quality | Step 7 · Injection Speed
05
Sufficient Shot Capacity
Define Shot Size & Screw Diameter
Shot Size Requirement
≥ Product weight × 1.35
Stability Principle
Product weight ≤ 75% of shot size
Consider cavity number
06
Injection Quality
Define Screw Compression Ratio & Injection Pressure
Engineering plastics
Require higher injection pressure
Proper screw compression ratio
Important Rule
Smaller screw diameter → higher injection pressure
Balance between pressure and plasticizing performance
07
Injection Speed
Define Injection Speed
Special requirements
Thin-wall products require high injection rate
Verify machine injection speed / rate
Trade-off principle
High pressure → lower speed
Low pressure → higher speed
Needs cross evaluation
Optimization Solution: Multi-Circuit System
Using dual or triple hydraulic circuits enables simultaneous composite actions (e.g., mold opening with ejection, plasticizing with cooling),
Dual-circuit system
Triple-circuit system
Synchronous actions

## Slide 7: SPECIAL CONSIDERATIONS
SPECIAL CONSIDERATIONS
Case 1 · Size Mismatch | Case 2 · High-Speed / Fast Machine Selection
01
Size Mismatch
Definition
A mismatch between mold size and injection requirements, including two situations: large mold with small shot demand, and small mold with large shot demand.
Large Mold / Small Shot
Solution: Standard clamping unit + small injection screw
Applicable when mold size is large but shot requirement is low.
Small Mold / Large Shot
Solution: Standard clamping unit + large injection screw
Applicable when mold size is small but shot requirement is high.
02
High-Speed / Fast Machine Selection
Core Objectives
Shorten molding cycle
Increase output
Reduce cost
Increase Injection Speed
Larger motor / pump
Accumulator (with closed-loop control)
Multi-Circuit System
Dual / triple circuits enable simultaneous actions such as mold opening, ejection,
and plasticizing.
Mold Optimization
Add cooling channels to improve cooling efficiency and shorten cooling time.
Notes
Performance improvement is accompanied by cost increase.
ROI evaluation should be conducted in advance to balance investment and return.

## Slide 8: Core Selection Logic & Key Principles
SUMMARY
Core Selection Logic
Information Collection
Step-by-Step Matching
Special Case Adjustment
Product-Centered Selection
All selection decisions should be based on the specific requirements of the product, ensuring that machine capability is highly aligned with production targets.
Balance Performance & Cost
On the premise of meeting production requirements,
equipment investment should be reasonably controlled to avoid over-configuration and resource waste.
Ensure Stable & Efficient Production
The ultimate goal of machine selection is to achieve long-term stable production efficiency,
maximizing equipment utilization and output benefits.
Scientific injection molding machine selection is the foundation of efficient production.
A systematic selection process ensures precise matching between equipment and requirements.
Professional Technical Guide
Scientific Selection · Efficient Production